## Slide 1
Muckpile Shape Prediction with a Physics-Informed AI Framework for Blast Modeling
Fei Zhang, Michael Gartley, Emmett Ientilucci
Introduction
What Happens When a Blast Unfolds
Blast control is vital to mining efficiency and safety. The muckpile—the rock pile left after a blast—shapes downstream loading and hauling performance. By fusing physics-based simulation with modern AI algorithms, our team aims to see seconds into the future: predicting the post-blast muckpile directly from the pre-blast terrain and explosive setup.
Blasting is an inherently complex process involving explosive detonation, rock fracturing, and gas–rock interactions.
t = 0s
t = 1s
t = 2s
t = ns
Field Recording
…
Blast Process by Time Scale
(seconds)
1e-7
1e-6
1e-5
1e-4
0.001
0.01
0.1
1
10
Non-Ideal Detonation
Elastic Hole Expansion
Nearfield Crushing
Equilibrium Pressure
Radial Tensile Fracturing
Fragmentation
Muckpile Formation
Mine Scale Vibrations
Burden Acceleration
Emulsion explosives
Charged blast-hole schematic
Example of a field blast setup with multiple charged boreholes.
Pre-Blast Terrain
Post-Blast Terrain
Before:
After:
Displacement Volume
Example of displacement evaluation using 3D models derived from drone videos and Structure-from-Motion.
IV. Physics–AI Co-Development Workflow
V. Prototype Experiments
Physics-based Simulation (Teacher)
End-to-End Machine Learning Model (Student)
MLP
Feature-grouped MLP
LSTM
Transformer
PINN
…
Simulation Engines
Blender (Bullet), MuSEN, …
Outputs
Fragment trajectories and final muckpile shape (t = N s)
Inputs
Blast configuration: pre-blast terrain, energy distribution, fragment geometry, rock and explosive properties, gravity…
Numerical Models
Finite Element Method (FEM) Computational Fluid Dynamics (CFD)
Discrete Element Method (DEM)
III. Muckpile Formation in 3D Models
Generate & Train
…
t = 0s
t = 1s
t = ns
…
Experiment #1: Single-point blast test. A cube model (100 shards) subjected to a single impulsive force field, simulating a localized explosion.
Experiment #2: Sequential-blast test. A bench-shaped model (2000 shards) subjected to two sequential impulsive force fields, simulating multi-point detonation.
Figure credits: (1) Austin Powder ; (2) O-Pitblast .
For more information, contact Fei Zhang at fzhcis@rit.edu, or visit https://github.com/fz-rit/blast-simulation-showcase